## Slide 1
UNIT -5 REPAIR AND MAINTENANCE
Preventive maintenance of the system:
Preventive maintenance is important to keep your computer running smoothly and to prevent potential issues from arising.
A preventive maintenance system refers to a proactive approach to maintaining equipment, systems, or infrastructure. It involves performing regular inspections, servicing, and repairs to prevent potential problems before they occur. The goal of preventive maintenance is to extend the lifespan of assets, reduce the possibility of unexpected failures, and minimize downtime.
Preventive maintenance for software:
Regular Updates: Apply patches and updates to software, OS, and dependencies.
Backups: backup your software this may help to recover when unexpectedly
remove from your system.
Performance Monitoring: Optimize performance and resource usage.

## Slide 2
4.Bug Fixes: Address errors and bugs and debugs(correct) them.
5.Documentation: Keep user and technical documentation up to date.
6.License Management: Ensure software licenses are current.
7.Compatibility Checks: Test for compatibility with new hardware or software.
8.Security Audits: Scan for vulnerabilities and viruses they may corrupt the software. .
These actions help prevent software failures and extend its lifecycle.

## Slide 3
Preventive maintenance for internal parts of a computer
Ensures optimal performance and extends the lifespan of hardware components. Key tasks include:
Cleaning: Regularly clean dust from internal components like the CPU, GPU, fans, and power supply to prevent overheating.
Checking Connections: Ensure that cables, connectors, and internal parts are properly seated and securely connected.
Cooling System Maintenance: Clean or replace fans, and check thermal paste on the CPU to prevent overheating.
Hard Drive Maintenance: Run disk checks and defragmentation (for HDDs) to ensure data integrity and prevent data loss.

## Slide 4
5.Power Supply Checks: Inspect the power supply for wear and tear, and ensure it's providing consistent voltage.
6.Memory (RAM) Checks: Run memory tests to identify faulty RAM modules and replace if necessary.
7.Component Upgrades: Periodically review internal hardware to upgrade outdated components for better performance.
8.Battery Checks (for laptops): Calibrate and replace batteries when their capacity depletes significantly.
These steps help in maintaining the computer's performance and preventing hardware failures.

## Slide 5
Preventive maintenance from dust:
Preventive maintenance to protect a computer from dust involves regular cleaning and protective measures to avoid dust buildup, which can cause overheating and component damage. Here's what you can do:
Regularly clean external and internal components.
Use compressed air to remove dust from internal parts like the CPU, GPU, and fans.
Clean fans and vents to maintain proper airflow.
Clean keyboard and mouse with compressed air or a soft brush.
Install dust filters on air intake vents and clean or replace them regularly.
Place the computer in a well-ventilated area, elevated from the ground.
Keep the computer away from dust sources like carpets or open windows.
Use dust covers for the computer and peripherals when not in use.
These actions help keep your computer dust-free and improve its performance and longevity.

## Slide 6
Power source in computer:
The power source for a computer is typically an external electrical supply connected to the computer through a power supply unit (PSU). The PSU converts alternating current (AC) from the mains into low-voltage direct current (DC) that the internal components of the computer use. In laptops, the battery serves as a power source when not connected to a direct power outlet. Stable and reliable power is essential for a computer's performance and longevity.
Power protection
Power protection in computers is crucial to safeguard the system from electrical disturbances that can damage hardware, corrupt data, or cause sudden shutdowns. Electrical problems such as power surges, outages, spikes, and fluctuations can affect a computer's sensitive components, making power protection devices essential for ensuring the system’s longevity and reliability.

## Slide 7
Power protection devices:
Surge Protectors: These devices shield the computer from power surges, which occur when there is a sudden spike in voltage. A surge can happen during lightning strikes or issues in the power grid. Surge protectors divert the extra voltage away from the computer, preventing damage to internal components like the motherboard, CPU, and hard drive.
How It Works: It contains components like metal oxide varistors (MOVs) that absorb and redirect excess voltage away from the connected devices.
2.Uninterruptible Power Supply (UPS): A UPS is a backup power device that provides temporary power to a computer in the event of a power outage. It allows users to save their work and shut down the system safely, preventing data loss. Additionally, a UPS can protect against voltage fluctuations and momentary dips in power, ensuring a stable power supply.

## Slide 8
How It Works: A UPS contains a battery that kicks in when the main power supply fails. It also often includes surge protection and voltage regulation functions to protect against power fluctuations and surges.
3.Voltage Regulators: Voltage fluctuations, such as under-voltage (brownouts) and over-voltage, can harm the computer’s components or cause instability. A voltage regulator ensures the computer receives consistent voltage, correcting the power supply when it deviates from safe levels.
How It Works: It monitors the incoming voltage and adjusts it to the required level, either by boosting low voltage or reducing high voltage.

## Slide 9
4.Power Conditioners: These devices clean the power by filtering out noise, spikes, and electrical interference that can affect the computer’s performance. Power conditioners ensure that the power entering the computer is stable and free of disturbances.
How It Works: It uses filters and other components to remove unwanted electrical noise and smooth out the power signal. This ensures that the power delivered to the computer is clean and stable.
By using these power protection solutions, computers are safeguarded against electrical risks, ensuring smoother operation, protecting valuable data, and prolonging the life of hardware components.

## Slide 10
Video card /Graphic card:
A video card, also known as a graphics card or GPU (Graphics Processing Unit), is a critical component in a computer responsible for rendering images, video, and animations. Here’s an overview:
Primary Function: The video card processes and outputs visual data to the computer’s display. It handles complex calculations related to image rendering and can significantly impact the quality and performance of graphics in applications and games.
Components:
  GPU: The core processor that performs the calculations needed for rendering images and video. It executes thousands of parallel operations to handle graphics tasks efficiently.
  Video Memory (VRAM): Dedicated memory on the graphics card used to store textures, frame buffers, and other data needed for rendering. VRAM allows the GPU to access data quickly, which is crucial for smooth graphics performance.
  Cooling System: Most video cards have fans or heat sinks to dissipate heat generated by the GPU during operation, ensuring stable performance and preventing overheating.
Example of graphics card: NVIDIA RTX 4090, AMD Radeon RX 7900 XTX, NVIDIA GeForce GTX 1660 Super, AMD Radeon RX 6600 XT, NVIDIA Quadro RTX 8000

## Slide 11
Core processor(GPU)

## Slide 12
Causes of video card failure:
Power Supply Issues: Inadequate or unstable power supply can cause power-related problems or failure of the graphics card.
Driver Problems: Outdated, corrupted, or incompatible drivers can lead to graphical glitches, crashes, or failure.
Physical Damage: Damage from improper handling, electrical shorts, or manufacturing defects can cause the card to malfunction.
Overheating: Insufficient cooling or dust buildup can cause the GPU to overheat, leading to damage or failure.
Dust and Debris: Accumulation of dust and debris in the GPU fans and heatsinks can impair cooling and lead to overheating.
Incompatible Hardware: Mismatched components or incompatible system configurations can cause issues with the graphics card.
VRAM Issues: Faulty or insufficient VRAM can result in graphical artifacts, crashes, or poor performance.

## Slide 13
Effects of graphic card failure in computer system:
- The screen may show artifacts, glitches, or be completely blank.
- Graphics-intensive applications and games may run slowly.
The computer may crash or freeze, particularly when performing tasks that depends
heavily on the GPU.
- Visual corruption in images, videos, or user interfaces can occur.
- Frequent error messages related to graphics drivers or hardware may appear.
- The screen resolution may drop, affecting the clarity and quality of visuals.
- General instability and unreliability of the system can result from a failing video card.
- Applications or games that depends on the GPU may not run or may not function correctly.

## Slide 14
Solution for video card issue:
Check Connections: Ensure that the video card is properly seated in the PCIe slot and that all power connectors are securely attached.
Clean the GPU: Remove dust and debris from the GPU fans and heatsinks to prevent overheating.
Update Drivers: Install the latest graphics drivers from the manufacturer’s website to fix compatibility issues and bugs.
Test with Another System: Test the graphics card in another computer to determine if the issue is with the card or other components.
Check Power Supply: Ensure that the power supply is adequate and providing stable power to the GPU.

## Slide 15
Run Diagnostic Tools: Use diagnostic software to check the health of the GPU and identify potential hardware problems.
Replace Thermal Paste: Reapply thermal paste if the GPU is overheating due to dried-out or degraded paste.
Reset BIOS/UEFI Settings: Reset or update BIOS/UEFI settings to ensure proper configuration of hardware components.
Perform a Clean Install: Uninstall existing graphics drivers and perform a clean installation to resolve driver conflicts.
Consider RMA or Replacement: If the card is still under warranty, contact the manufacturer for a replacement or repair.

## Slide 16
Causes of image quality problem in monitor:
An image quality problem in monitor can caused by many reason such as poor resolution setting, mismatched cable connection or dirty screen.
Resolution Mismatch: Using a resolution setting that does not match the monitor’s native resolution can cause blurriness or distortion.
Poor Connection: Loose, damaged, or improperly connected cables can lead to poor image quality, such as flickering or artifacts.
Driver Issues: Outdated or corrupted graphics drivers can affect display performance and quality.
Monitor Settings: Incorrect brightness, contrast, or color settings can impact the overall image quality.
Hardware Issues: Problems with the monitor itself, such as dead pixels, backlight bleeding, or aging components, can lead bad image quality.
Graphics Card Problems: Issues with the graphics card, such as overheating or malfunctioning, can affect how images are rendered on the monitor.

## Slide 17
How to fix screen resolution/image quality issue in monitor:
To fix image quality or resolution issues on a monitor, you can follow these steps:
Check Resolution Settings: Ensure that the monitor’s resolution setting matches its native resolution. You can adjust this in the display settings of your operating system.
Update Graphics Drivers: Install the latest drivers for your graphics card from the manufacturer’s website to fix compatibility issues and improve performance.
Adjust Monitor Settings: Use the monitor’s on-screen display (OSD) menu to adjust brightness, contrast, colour settings, and sharpness to improve image quality.

## Slide 18
Verify Cable Connections: Ensure that all video cables (HDMI, DisplayPort, DVI, VGA) are securely connected and not damaged. Try using different cables if necessary.
Check Refresh Rate: Set the monitor’s refresh rate to the recommended value in the display settings of your operating system.
Reset Monitor Settings: If all else fails, reset the monitor to its factory default settings using the OSD menu.
Test with Another Device: Connect the monitor to a different computer or device to determine if the issue is with the monitor or the original system.
By systematically addressing these areas, you can often resolve image quality or resolution problems and restore proper display performance.

## Slide 19
Input/Output connection issue causes:
The functioning of the computer system is based on the combined use of input and output devices. An input device allows us to tell the computer to perform an action and the devices returns an action via an output devices.
Due to some factor that cause the input out issue . Such as :
Loose or unsecured cables. Damaged cables.
Faulty or damaged ports. Outdated or corrupted drivers.
Incompatible hardware. Insufficient/unstable power supply.
Software conflicts or OS issues. Outdated/corrupted firmware.
Physical damage to connectors or ports. Incorrect system or BIOS/UEFI settings.

## Slide 20
Solution for Input/Output connection issues solution :
Input and output device connection issues can be caused by a variety of factors, here are some steps you can take to try and fix the problem:
Check the connection of the device to the computer, make sure that the cables are securely plugged in and that the connectors are not damaged.
Check the power supply of the device, make sure that it is connected to a power source and that it is turned on.
Check the device's settings, make sure that it is configured correctly and that it is set to the correct input or output mode.
Check for any software updates for the device and the computer.
Try different USB ports, sometimes the USB ports can malfunction.
Try a different cable, sometimes the cable can be faulty.
Try disabling and re-enabling the device in the device manager.

## Slide 21
Processor
The processor, or central processing unit (CPU), is the brain of a computer, responsible for executing instructions and performing calculations that drive software applications and system operations. Here’s a brief overview:
Function: The CPU processes data and instructions from software and hardware. It performs tasks such as arithmetic calculations, data manipulation, and control operations to run programs and manage system functions. The main function of processor are fetch( fetching instruction from system RAM) , decode(instruction are converted into understanding form) and execute(operation are performed).

## Slide 22
Types of processor:
1.Microcontroller: A microcontroller is a type of small computer designed specifically to perform single tasks. It includes a CPU (Central Processing Unit), memory (RAM, ROM), and input/output pins all on a single chip. Microcontrollers are typically used in automated devices, electronic gadgets, and control systems. For example, microcontrollers are used in devices like washing machines, microwave ovens, TV remote controls, etc.
2.Embedded Processor: An embedded processor is designed to perform specific tasks within a computer system. It is used as part of a larger system, where it is responsible for executing one or more dedicated functions. For example, embedded processors are used in sensors in smartphones, industrial machines, and medical devices. The processor in these devices performs specialized tasks, such as measuring speed, controlling temperature, or processing data.

## Slide 23
3.Digital Signal Processor (DSP): A Digital Signal Processor (DSP) is a special type of microprocessor that processes signals digitally. Its primary function is to convert analog signals (such as sound, video, or temperature) into digital form and then rapidly compute and analyze those signals. For example, DSP is used in mobile phones for voice filtering, in music players for sound enhancement, in digital cameras for image processing, and in radar systems for signal analysis.
4.Media Processor: A type of processor designed specifically for handling media-related tasks, including video decoding, encoding, and playback. Media processors are used in devices like smartphones, digital cameras, and media streaming devices to handle complex media operations efficiently.

## Slide 24
5.Microprocessor: The central processing unit (CPU) of a computer system, capable of executing a wide range of general-purpose tasks. Microprocessors are the main component of personal computers, laptops, and servers, and they handle various computing operations and system management functions.
Voltage level:
Voltage level refers to the amount of electrical potential difference between two points in an electrical circuit. It is measured in volts (V) and indicates the "pressure" that drives electric current through a conductor. Voltage levels can vary depending on the system or device, ranging from low voltage used in small electronics to high voltage in power transmission systems. modern CPU
Operates on the range of 1.0 to 1.5 volts while mobile CPU operates around 0.8v to 1.3 volt.

## Slide 25
Types of Voltage Levels:
Low Voltage: Typically refers to voltages below 50V. Low voltage is used in devices like smartphones, computers, and household electronics.
2. Medium Voltage: Ranges from 1kV (1,000V) to 35kV. This is commonly used in distribution systems to transfer electricity from substations to consumers.
3. High Voltage: Voltages above 35kV are considered high. High voltage is used in transmission lines to carry electricity over long distances with minimal loss.
4. Extra-High Voltage (EHV): This involves voltages above 230kV, typically used in long-distance, high-capacity power transmission.

## Slide 26
Importance of Voltage Levels:
Safety: Different voltage levels come with different risks. Low voltages are safer to handle, while high voltages can be dangerous and require specialized equipment and protection.
Efficiency: High voltage transmission is more efficient for long distances, as it reduces energy loss due to resistance in conductors.
Device Compatibility: Electronic devices are designed to operate at specific voltage levels, and exceeding those levels can damage the device or reduce its lifespan.
Understanding voltage levels is crucial for ensuring the safe and efficient design and operation of electrical systems.

## Slide 27
Introduction to Processor cooling:
Processor cooling is the process of removing heat from the processor (also known as the central processing unit or CPU) in a computer. The processor is one of the most heat-sensitive components in a computer, and if it becomes too hot, it can cause the computer to malfunction or even become damaged.
Method/techniques for processor cooling:
If the processor is cooling as needed , it helps to perform operation smoothly to the processor . Here are some techniques how we maintain the processor cool:
Heat sink:
A block of metal (usually aluminium or copper), metal bars of metal fins that attach to be processor or other motherboard components. Heat from the processor is transferred to the heat sink and then blown away by the air flow throughout the computer case.

## Slide 28
2. Fan: Fans can be attached to the processor , to the side of the processor and to the case. It regularly provide air to the processor during system is on state.
3. Thermal paste: Thermal paste compound or grease is applied to the top of the processor before a heat sink is attached. A thermal compound applied between the CPU and heatsink to fill microscopic gaps and improve thermal conductivity.
4. Liquid cooling: Liquid is circulated through the system via a heat sink mounted on the CPU. Heat from the processor is transferred to the cooler liquid.
5. Heat pipe: A metal tube used to transfer heat away from an electronic component. Heat pipes use a sealed, evacuated tube with a small amount of liquid. As heat is applied, the liquid evaporates, moves to the cooler end of the pipe, and condenses back into liquid. This cycle efficiently transfers heat from the CPU to a heatsink or radiator. Especially used in laptop.

## Slide 29
6.Processor socket and slot:
The processor socket (also called CPU socket) is the connector on the motherboard that houses a CPU and forms the electrical interface and contact with the CPU. Processor sockets use a pin-grip array (PGA) where pins on the underside of the processor connect to holes in the processor socket.
7. Peltier (Thermoelectric) Cooling
Utilizes a thermoelectric module (Peltier device) that creates a temperature difference when electrical current flows through it. One side of the module becomes hot while the other side becomes cold.

## Slide 30
System cooling :
It refers to the methods and technologies used to dissipate heat generated by various components in a computer, such as the CPU, GPU, and power supply. Effective cooling ensures that the system operates within safe temperature limits, preventing overheating and maintaining optimal performance.
Why System Cooling is Needed:
Prevents overheating and hardware damage
Maintains optimal performance
Ensures system stability
Increases component lifespan
Avoids automatic shutdowns due to high temperatures
Reduces energy consumption
Prevents performance throttling during heavy workloads

## Slide 31
Ventilation:
Ventilation refers to the process of introducing fresh air into an enclosed space and removing stale or contaminated air. In the context of computers, ventilation refers to the flow of cool air into the computer case and the movement of hot air out of the case. Adequate ventilation is necessary to ensure that the internal components of the computer are kept at a safe temperature and to prevent overheating.
Why ventilation is needed?
Prevents overheating of internal components.
Enhances system performance and longevity.
Reduces the risk of hardware damage due to high temperatures.
Promotes airflow, removing heat generated by the system.
Reduces fan noise by allowing more efficient cooling.
Improves stability and reliability during high-intensity tasks

## Slide 32
Computer virus background:
A computer virus is a type of malicious software designed to replicate itself and spread from one computer to another, often without the user's knowledge. The concept of computer viruses dates back to the early days of computing in the 1970s and 1980s. The first computer virus in the world is generally considered to be the Creeper virus, which was created in 1971. It was an experimental self-replicating program written by Bob Thomas, an engineer at BBN Technologies. When a computer was infected by Creeper, it would display the message: "I'm the creeper, catch me if you can!" It did not cause harm to files or data, but it is widely considered the first example of a virus-like program.

## Slide 33
Virus detection:
Virus detection involves identifying and removing malicious software (viruses) from computer systems. This is an information security process aimed at checking for and identifying dangerous viruses and program . This is the most important features of antivirus software. Modern antivirus software uses several techniques to detect viruses, each with its own strengths:
1.Signature-based detection: The antivirus compares files on the computer to a database of known virus signatures (unique patterns). This is the most common method but only works for known viruses.
2.Heuristic analysis: This method looks for suspicious behavior or code that resembles known viruses, allowing it to detect new, previously unknown viruses or variants. It helps find zero-day threats.
3.Real-time scanning: This continuously monitors files and network activity to detect and block viruses as they enter the system. It's essential for preventing infections from spreading.

## Slide 34
4. Machine learning: Some modern antivirus software uses AI and machine learning to detect patterns and predict potentially harmful programs, even if they don't match existing virus signatures.
5.Behavioral detection: Rather than analyzing code, this method monitors the behavior of programs in real-time. If a program exhibits virus-like behavior (e.g., trying to modify system files or spreading to other programs), it is considered as virus .

## Slide 35
Types of computer viruses
1. File Infector Viruses
These viruses attach themselves to executable files, such as .exe or .com files. When the infected file is executed, the virus activates and spreads.
Example: The Cascade Virus is a well-known file infector that causes text to fall or "cascade" down the screen.
2. Macro Viruses:
Macro viruses target software applications, particularly those that use macros, like Microsoft Word or Excel. They are often embedded in documents, activating when the document is opened.
Example: Melissa Virus, which spread via email attachments and caused widespread disruption in the late 1990s.

## Slide 36
3. Boot Sector Viruses: These viruses infect the master boot record (MBR) of a computer’s hard disk or other storage devices, making them difficult to detect and remove. They activate when the computer starts.
Example: Stone Virus, an early boot sector virus, infected the MBR, causing disruption at the operating system level.
4. Polymorphic Viruses: These viruses change their code each time they infect a new system, making it harder for antivirus software to detect them. They are known for their adaptability and stealth.
Example: Storm Worm, which constantly modified itself to evade antivirus detection.

## Slide 37
5. Multipartite Virus:
These viruses use multiple methods to infect systems, targeting both the boot sector and files, which makes them harder to detect and remove.
Example: Tequila Virus, which used a combination of file and boot sector infection methods.
6. Resident Viruses: Resident viruses embed themselves in a computer’s memory, allowing them to execute without user intervention. They remain active even if the original infected program is closed.
Example: Randex, which loads itself into memory and then monitors computer activities.

## Slide 38
7. Direct Action Viruses:
These viruses don’t embed in the system memory; instead, they attach to specific files. When activated, they spread quickly but are easier to remove since they don’t hide in memory.
Example: Vienna Virus, which simply attaches to files and runs only when those specific files are executed.
8. Ransomware(Malware):
Ransomware encrypts the user’s files, making them inaccessible until a ransom is paid to the attacker. It often spreads through phishing emails or infected downloads.
Example: WannaCry, a large-scale ransomware attack that impacted computers globally.

## Slide 39
9.Email virus :
it is malware that spreads via email, often through infected attachments or malicious links. When a user clicks the link or opens the attachment, the virus can infect their device, damage files, and spread to other contacts. Notable examples include the Melissa and ILOVEYOU viruses. To prevent infection, avoid suspicious attachments, verify links before clicking, use antivirus software, keep systems updated, and be cautious of phishing emails.

## Slide 40
Symptoms of computer when affected by virus:
1.Slow system performance or frequent crashes
2.Unexpected pop-up ads or error messages
3.Programs start or close on their own
4.Files or data become corrupted or disappear
5.Increased network activity without explanation
6.Unusual messages or files sent to contacts
7.Inability to access certain files or programs
8.Web browser redirects to unknown websites
9.Disabled antivirus or security software
10.High CPU or disk usage with no apparent cause
11.Appearance of unfamiliar icons or programs
12Computer freezes or becomes unresponsive

## Slide 41
Ways to virus transfer:
Computer viruses can spread through various means, primarily when users unintentionally download or transfer infected files or media. Here are some common ways viruses are transferred:
Email Attachments: Malicious emails may contain infected attachments. When users open these files, the virus can be installed on the computer.
Malicious Links: Links in emails, messages, or websites can lead to malicious websites or downloads. Clicking these links can trigger a virus download without the user’s knowledge.
Infected Software or Files: Downloading software, files, or media from untrusted sources can introduce viruses if the content has been tampered with.
Removable Media (USB Drives): Inserting an infected USB drive or other removable media can transfer viruses. Some viruses can auto-execute when the drive is inserted.
File-Sharing Networks: Peer-to-peer (P2P) networks, like those used for torrenting, often contain infected files, and downloading from these sources can introduce viruses.

## Slide 42
6.Fake Software Updates: Some viruses are disguised as legitimate software updates, especially for commonly used applications. When users install these “updates,” they unknowingly install the virus.
7.Infected Websites (Drive-by Downloads): Visiting compromised or malicious websites can sometimes lead to automatic downloads of viruses if the browser or security software is outdated.
8. Network Propagation: Viruses can spread through shared networks, especially if devices are not adequately protected by firewalls or antivirus software. Once inside the network, viruses can move between devices.
Having strong antivirus software, being cautious of suspicious links or emails, and keeping systems updated can help prevent virus transfers.

## Slide 43
Antivirus software
It is a program designed to detect, prevent, and remove malicious software, such as viruses, worms, Trojans, and other forms of malware. It plays a crucial role in safeguarding computers and networks from cyber threats by scanning, identifying, and neutralizing malicious code before it can cause harm.
Using antivirus software is essential for maintaining the security and integrity of computer systems, preventing data loss, and protecting personal and sensitive information from cybercriminals. Regular updates and scans ensure that antivirus programs can handle new and evolving threats.

## Slide 44
Protection method from computer virus:
A computer that is not secured is similar to an open door for computer viruses. Antivirus programs have come a long way in identifying and preventing the spread of computer viruses. However, if your device is infected, we recommend installing an antivirus solution to remove it.
Take these steps to protect your PC with the best computer virus protection:
Install reliable antivirus software: Use reputable antivirus programs and keep them updated to detect and remove viruses.
Keep software updated: Regularly update your operating system, applications, and security software to patch vulnerabilities.
Enable firewalls: Use a firewall to block unauthorized access and potential threats from external sources.
Avoid suspicious emails and links: Do not open attachments or click links from unknown or untrusted sources.

## Slide 45
Download from trusted sources: Obtain software and files from reputable websites and avoid pirated or unverified sources.
Use strong, unique passwords: Employ complex passwords and change them regularly to protect against unauthorized access.
Be cautious with removable media: Scan USB drives and other removable media for viruses before opening files.
Practice safe browsing: Avoid visiting dubious websites and use browser security extensions to enhance protection.